## Slide 1: iCatching
An Automated Soft Robot Catcher
Tom Queen
Daniel Turner
Demetrius Zaibo

## Slide 2: Cable Driven Machines
Cables typically serve three roles
  Manipulation from afar
    Quick release mechanisms
    Fishing line
  Antagonistic control
    Muscles & Tendons
    Surgical Manipulator
  Power to speed transfer
    Windlass
    Pulleys

## Slide 3: Previous Catcher-Bots
Table tennis: nearly catcher-bots
Humanoid / Robot Arm: highly complex, but possibly able to adapt more readily
Quadcopter: Highly versatile, and as complex as humanoids. Using a hammer to crack an egg
2D catchers: Much simpler
  Double inverted pendulum
  2D frame

## Slide 4
ERROR:
Too many grippers!
Previous Gripper Designs
Hard
Soft
Passive
Active
Notes: Hard Passive: Bin, table tennis racket, wall, brick
Hard Active: Industrial grippers, e.g. MakeBlock
Soft Passive: Crumple zones, air bags, velcro
Soft Active: Coffee beans, Festo, Electro-adhesion, Pneumatics, Adaptive Compliance … and more!!!

## Slide 5: Our Gripper Designs
Active: Festo Fin Gripper
  Requires knowledge of time to close just before the object hits the gripper
Passive: Funnel Catcher
  Careful design, limited range of objects it can catch, reduced control complexity

## Slide 6: Design
Passive Gripper FEA
Active Gripper CAD
Frame
Motors…

## Slide 7: Motors
Problems
Gear Box:
  Gears slipping and plastic failing
    Reducing gear ratios
    Increasing gear depths to increase surface area of contact between teeth
    Reducing tolerances & adding blocks to reduce side movement
    Strengthen gearbox design
Stepper Motor + Driver
  Unable to deliver power and difficult to control
    Attempted reusing an old controller via sniffing commands from an XP machine
    Attempting to use different controllers

## Slide 8: Object Tracking
Generic Algorithm
  Attempted 3 algorithms
    Histogram centric
    Optical flow based
    Neural-network inspired
Simple Algorithm
  Colour detection with centre of mass
Integration with ROS

## Slide 9: To Do
Look into image stabilization & Kalman filter
Finish system kinematics
Attempt PID control

## Slide 10: Questions?