## Slide 1: iCatching
Showcase Presentation
Tom Queen
Daniel Turner
Demetrius Zaibo

## Slide 2: Background
What are catching robots?
  Machines which automatically grasp or intercept a target moving object
How could they be useful
  Toys
  Sports training
  Robotic assistants on space walks
  Impromptu conveyor systems over uneven terrain

## Slide 3: Body - Design
Cartesian frame design
  Conceptually simple
Bungee cord
  Non-linear elasticity
  Variable tension control
Spool
  Recycling 3D printer filament spools

## Slide 4: Body - Motors
Micromotors E192-2S
  High torque but very slow!
  Designed a gearbox: hard to get right with 3D printing
Stepper motors
  Great specifications
  Poor performance using the original motor driver
  Poor control & slippage with alternative driver
Dynamixel MX-64
  Slower speeds & daisy chain coms issues
  Out of the box solution though
  Multithreading / parallel communications

## Slide 5: Body - Throwing
Motors can’t handle pullback torques!
Solution: clamps!
Slow motor can be used to pullback

## Slide 6: Gripper and Cameras
Passive gripper – egg-drop inspired design
  FEA used to tune the design
Active gripper – FESTO inspired design
  Deformable – can grasp a variety of objects
  Tried and tested
Eye-in-Hand solution
  Cables already needed to actuate the gripper
  Simplifies the control for quicker turn-around

## Slide 7: Vision - Attempted
Attempted several “generic” solutions
  Changing Histograms
    Changing lighting conditions
  Optical Flow
    Lateral motion dominance and slow
  Pyramidal Scaling
    Lateral motion dominance and noisy
  YOLO
    Slow (15fps max!)

## Slide 8: Vision - Solution
Settled on simplicity – colour thresholding
  Insert steps here?
Result had inconsistencies
  Kalman filtering to interpolate and smooth

## Slide 9: Control
Kinematics
  Cord length velocities are dependent on the gripper position
  Considers tension separately
Processors
  Teensy used for encoded motors & steppers
  Laptop used for everything else

## Slide 10: Control
Communications
  ROS used to pass data between major code blocks and processors
  Stepper motor libraries on Teensy
  OpenCV links to camera
Stepper motor stress testing
  Very important test – can it play Green Hill Zone?

## Slide 11: Results
Demo Time
=D

## Slide 12: Questions?